## Slide 2
Mobile Plant & Fixed Plant Safety - Quarries
Extractive Industries Ireland
Date: 26/09/2018
Cormac McCarthy – Roadstone Ltd

## Slide 3: Isolation of Plant and Equipment

## Slide 4: Isolation of Plant and Equipment
Plant must be isolated and locked out before guards or safety devices are removed
Each person must attach their own lock(s)
LOTOC – Lockout, tag out and confirm by attempting to start the equipment once it is isolated

## Slide 5: Isolation of Plant and Equipment
Padlocks and tags can only be removed when;
All safety guards are back in place
All workers are positioned safely for start up
The machine is ready and safe for operation

## Slide 6: Guarding & Isolation
Fixed panel type guards
Access gates should be electrically interlocked.
Remote greasing to enable lubrication to be carried out without entering the guarded area.

## Slide 7: Isolation & Interlock
Isolator & Captive Key
Key Exchange Unit
Access Interlock

## Slide 8: Isolation & Interlock
Isolator & Captive Key
Key Exchange Unit
Access Interlock

## Slide 9: Isolation & Interlock

## Slide 10: Isolation of Plant and Equipment
Energy Isolation (sources of energy)
Electrical
Pneumatic
Hydraulic
Mechanical / Gravitational
Thermal
Residual energy in machine component parts
Material flow

## Slide 11: Vehicle Safety
Mirrors
Reverse Beeper / Motion Beeper
Beacons
Reversing Camera / Radar
High-vis Clothing
Under-run Barriers
Handbrake Alarm

## Slide 12: Vehicle Safety – Under-run Barrier

## Slide 13: Vehicle Safety

## Slide 14: Forklift Safety
Forward and reverse blue light system

## Slide 15: Vehicle Safety - Battery Safety
Use from
Battery Booster to machine
Machine to machine (surge protection)
Battery Booster

## Slide 16: Vehicle Safety - Battery Safety

## Slide 17: Vehicle Safety - Battery Safety

## Slide 18: Vehicle Safety - Battery Safety
Boosting Point Label for 12 Volt or 24 Volt must be fitted on the machine.

## Slide 19: Vehicle Safety - Battery Safety
Electronic Battery Tester
Old type tester.
Applies Load - DANGEROUS

## Slide 20: Vehicle Safety – Tyre Inflation
Automatic Tyre Inflator

## Slide 21: Vehicle Safety – Tyre Inflation
Tyre Pressure Charts

## Slide 22: Vehicle Safety – Body Props

## Slide 23: Vehicle Safety – Body Props

## Slide 24: Vehicle Safety – Body Props

## Slide 25: Vehicle Safety – Body Props
Skid Steer
180° Excavator
Dumper Truck Body

## Slide 26: Work at Height
Fall Prevention

## Slide 27: Hierarchy of Control Measures

## Slide 28
Thank You