## Slide 1: Bitumen Delivery and Storage
Gearoid Lohan
Hazards of Bitumen Delivery and Storage

## Slide 2: Overview
Bitumen regarded as a ‘safe product’
Inert at ambient temperature.
Low Volatility
Low water solubility
Highly durable

## Slide 3: Bitumen Types and Grades
Penetration grade bitumens 40/60pen, 70/100pen, 160/220pen
Polymer Modified Grade Bitumens Special Applications – Higher Temperatures
Oxidised / Blown Grade Bitumens
Clear Grade bitumen (Coloured Asphalt)
Other types Emulsions Hard Grades

## Slide 4: Schematic of the Asphalt Value Chain
Upstream:
Crude Exploration &
Production
Shipping / Supply:
Crude is moved by ship or
Pipeline to refineries
Downstream: Refinery
Crude
Crude
Refined Products:
Bitumen
Modification
Processes
Bitumen:
Supply & Distribution
Bitumen
Asphalt
Plant
Or Emulsion Manufacture
Transport
To work site
Asphalt
Asphalt
Paving

## Slide 5: Bitumen – The Hazards
High handling Temperature – Bitumen Burns.
Fire – Combustible
Contact with Water
Bitumen Overflow during off-loading
Pressure discharge
Vapour emissions (11oc drop – reduces fumes by 50%)

## Slide 6: The Hazard - Fire
Flash Point > 230 oC (approximately)
Contact with Insulation (self ignition)
Overheating
Never use water – foam or dry powder to extinguish the fire.

## Slide 7: The Hazard – Bitumen Burns
locations
Hose
Overflow
Valve Blocked
Sampling
Treatment
Cool for 5 minutes (water)
Never attempt to peel off bitumen

## Slide 8: The Hazard – Pressure Discharge
50% of all accidents – during delivery.
Can lead to Bitumen Burns
Drench Shower
Bitumen Hoses –Testing, Flanges

## Slide 9: The Hazard – Bitumen Spills
Tank Gauges
High Level Alarms
Overflow pipe

## Slide 10: Minimize the Risk
Drench Shower
PPE - within 6m of the delivery point.
Product storage temperature
Tank Labeling avoid product crossover
Level gauge maintenance
Bitumen First Aid – Bitumen Burns Cool water (Drench Shower) Leave bitumen in place Do not bandage Call emergency Services

## Slide 11: Bitumen HSE – What the Bitumen Tank Farm should have?
Off-loading Instructions
Adequate Lighting
Tank Labelling, Gauges, Alarms
Bitumen Burns poster
Bitumen Burns Guidance
Never mix penetration grade
with cutback
Adequate Turning Angle for Trucks

## Slide 12: Bitumen PPE
Helmet, Visor and Neck apron
One piece Coverall - with High Vis
Heat resistant gloves
Foot protection

## Slide 13: Bitumen HSE – What the Bitumen Tank Farm should have?
Adequate Turning Circle
Drench Shower
Fire Extinguisher
Material Safety Data Sheets
Emergency Plan
Tel No.s – Do you know where to go in the event of an emergency ?
Risk Assessment
Adequate Signage/Posters - Directions